## Slide 2: Obstacle Detection System – Black box
Purpose: To detect and locate obstacles inform navigation decisions.
Requirements:
  Detect obstacles within the range constraints of the HC-SR04 sensors (2cm – 400cm)
  Output the grid reference location of detected obstacles to the navigation system
External Interfaces:
  INPUT: Location System
    Current location
    Current heading angle
  OUTPUT: Navigation System
    Grid reference of detected obstacle

## Slide 3: Obstacle Detection System - Internal
Requirements:
  Detect obstacle distance with accuracy of : based on obstacle grid reference calculation method
  Convert AVS location, heading and sensor data into obstacle grid reference
  Internal Interfaces:
    Hardware-Software: HC-SR04 data
    Hardware-Software: Temp/humidity

## Slide 4: Obstacle Detection System - Risks
Detection distance error :
  Consequence: grid references may be incorrectly calculated
  Solution: upon testing if this issue emerges, using temperature and humidity to improve accuracy.
  In first instance not doing due to cost-benefit analysis as estimated errors are within limits

## Slide 5: Obstacle Detection System - Risks
Software uses > 20% on board Arduino resources:
  Consequence: May not be enough resources for all sub-system scripts
  Mitigation: Apply efficient programming principles
  Solutions:
  1. Purchase a Teensy

## Slide 6: Obstacle Detection - Risks